## Slide 1
WELCOME
TO THE JULY EDITION
OF THE 2019
M&R SEMINAR SERIES

## Slide 2: BEFORE WE BEGIN
SAFETY PRECAUTIONS
  PLEASE FOLLOW EXIT SIGN IN CASE OF EMERGENCY EVACUATION
  AUTOMATED EXTERNAL DEFIBRILLATOR (AED) LOCATED OUTSIDE
PLEASE SILENCE CELL PHONES OR SMART PHONES
QUESTION AND ANSWER SESSION WILL FOLLOW PRESENTATION
PLEASE FILL EVALUATION FORM
SEMINAR SLIDES WILL BE POSTED ON MWRD WEBSITE (Link to be provided soon as the District website was just updated recently )
STREAM VIDEO WILL BE AVAILABLE ON MWRD WEBSITE (Link to be provided soon as the District website was just updated recently )

## Slide 3: Erik R. Coats, P.E. Ph.D.
Dr. Erik R. Coats is a Professor of Environmental Engineering at the University of Idaho, and is a licensed professional engineer in Oregon, Washington and Idaho. Prior to earning his doctorate, Dr. Coats spent 13 years working as a professional engineer designing municipal water and wastewater systems. His expertise is in the area of biological wastewater treatment and waste resource recovery systems. At the University of Idaho Dr. Coats is focused on advancing microbial processes for upcycling industrial/municipal/agricultural waste streams to high-value commodities, and developing an enhanced molecular-level understanding of biological nutrient removal processes.
To date his research team has advanced a biotechnology for producing biodegradable plastics on dairy manure (and other waste streams, including sugar beet waste; tomato cannery waste; and municipal wastewater), with commercial application on the horizon. The process integrates with anaerobic digestion for bioenergy production, but can also be deployed independently. Dr. Coats' research team also has conducted extensive research into the wastewater resource recovery process known as enhanced biological phosphorus removal (EBPR), with current efforts additionally focused on short-cut nitrogen removal integrated with EBPR.

## Slide 4: 2019 seminar series Research presentation: ebpr (incl. ras fermentation) & biological nutrient removal
July 26, 2019
Metropolitan Water Reclamation District of Greater Chicago
Erik R. Coats, P.E., Ph.D.
Professor of Civil and Environmental Engineering

## Slide 5: Coats’ professional background
BSc (1990), MSc (1992): University of Idaho
1992-2002: Engineering consultant, Portland, OR. region
Licensed PE in Idaho, Oregon, Washington
PhD (2005): Washington State Univ. (Dr. Frank Loge, major prof.)
2006: joined UI as Assistant Professor
2012: tenured, promoted to Associate Professor
2018: promoted to Professor

## Slide 6: Coats’ research emphasis
Biological Nutrient Removal:
  Phosphorus removal (EBPR); nitritation
Resource Recovery: emphasis on polyhydroxyalkanoates (bioplastics)
Anaerobic Digestion
Appropriate blend of fundamental and applied
Integrate molecular methods

## Slide 7: Coats environmental engr. lab
Molecular capabilities:
qPCR
PCR
DNA sequencing
Proteomics
Transcriptomics
Metabolomics
multi -Omics

## Slide 8: Coats environmental engr. lab
Comprehensive analytical capabilities:
PHA; VFAs; nutrients; CH4; solids characterization
PLC-controlled operations

## Slide 9: Always use real wastewater
Currently >80 gallons weekly
Also ferment primary solids

## Slide 10: Bench to Pilot scale

## Slide 11: Topics for today
Sharing progress on and status of…..
EBPR/RAS fermentation
Insights on critical EBPR metabolisms
BNR & Nitritation studies

## Slide 12: Studying ebpr
Many challenges with EBPR….
  What are PAOs? How to maximize enrichment?
  Optimal operating conditions?
  Best carbon source? Ensuring sufficient carbon?
  How to achieve/ensure process stability, resiliency?
  Why does the EBPR ‘fail’? How to induce ‘recovery’?
My group’s research focus….
  Build from known process fundamentals, principles
  Be pragmatic, practical – how can results be effectively translated?
  Carefully validate empirical observations
  Focus on mixed culture function over phylogenetic structure

## Slide 13: What is EBPR?
Biological process targeting near-complete recovery of wastewater PO4
Cycle MLSS through anaerobic – aerobic zones
Enrich for PAOs
  Uptake and store excess PO4 as polyphosphate

## Slide 14: brief refresher on core ebpr principles

## Slide 15: Ebpr Carbon sources
EBPR fundamentally centers on VFAs….potential sources:
  Primary solids fermentation
  Ferment imported organic matter
  Generated in collection system
  Purchase
  RAS fermentation?
Other forms of useful carbon?

## Slide 16: VFAs and Pha synthesis
Valeric Acid
Propionic Acid
Acetic Acid
Butyric Acid
Polyhydroxyvalerate (PHV)
Polyhydroxybutyrate (PHB)

## Slide 17: Are all vfa’s the same??

## Slide 18: Are anaerobic conditions necessary?
No evidence to the contrary
Indeed: excess NO3 in RAS has been shown to induce BPR failure

## Slide 19: What and who are paos?
Bacteria with specific metabolic capabilities capable of accumulating excess orthophosphate
VFAs PHA PHA Glycogen P PolyP
No consensus that a PAO is a single species.
  Could be comprised of several different bacterial groups…..but, cannot isolate PAOs
HOWEVER, in quantifying PAOs: methods currently based on the model bacterium “Candidatus Accumulibacter phosphatis”
Anaerobic-Aerobic Cycling

## Slide 20: are all ebpr bacteria the model Pao?
Research suggests that EBPR bacteria are more than simply “Candidatus Accumulibacter phosphatis”
Only bacteria grown on synthetic wastewater aligned well with “Candidatus Accumulibacter phosphatis”
Tetrasphaera only detected in crude glycerol-fed EBPR reactor (1.9%)
  Only 0.3% in Moscow EBPR……with VERY long anaerobic HRT

## Slide 21: Ebpr and ras fermentation
Published in Water Environment Research, 7/18

## Slide 22: Our Ras fermentation research
Viewing “RAS Fermentation” through a literal metabolic lens….
Fermentation occurring on the “substrate” (i.e., RAS) immediately preceding the word “fermentation”
Phase 1 – batch RAS fermentation studies
Phase 2 – integrate RAS fermentation within an EBPR configuration
Evidence of VFA production?
Enhance EBPR performance?

## Slide 23: Phase 1 research evaluate ras fermentation
Source #1 – Moscow, ID water resource recovery facility (WRRF)
  A2/O process, with an oxidation ditch
    Nitrification, pre-anoxic denitrification, and biological phosphorus removal
  RAS: 5500-7600 mgTSS/L
  pH 7.0-7.25
Source #2 – Pullman, WA WRRF
  Modified Ludzak Ettinger (MLE) process
  Nitrification and pre-anoxic denitrification
  RAS: 18000 mgTSS/L; pH ~ 7.0
Bench-scale, batch reactors
  20-22˚C

## Slide 24: Fermenting Moscow ebpr Ras effect on soluble phosphorus
“Typical” anaerobic P release
  > 10 mgP/L…..rapidly
RAS fermentation P release
  < 2 mgP/L in 1st two hours
  AND…..much higher TSS concentration than typical MLSS
EBPR P release is associated with….
  Energy production
  In support of VFA consumption
Data suggests little-to-no VFA production
Typical AN-AE EBPR and P cycling

## Slide 25: Fermenting Moscow ebpr Ras effect on carbon
No observed VFA accumulation
PHA production
  None during 1st 300 minutes
  Ultimately 40-50 mgPHA/L
    Predominantly polyhydroxyvalerate (PHV)
  5 carbon PHA – synthesized from even/odd carbon VFAs
  Suggests fermentation of cells – lipids
Carbon data aligns with P data
  0-300 minutes: P release not associated with EBPR
  EBPR metabolisms MAYBE induced after 300 minutes

## Slide 26: Fermenting Pullman mle ras
Comparable “deep” anaerobic conditions
Rate of P release 2.5-5 greater than Moscow EBPR RAS
No PHA synthesis
VFAs
  No production for 1st 7.5 hrs
  Ultimately ~ 530 mg VFAs produced
    50% acetic acid
    20% propionic acid
    16% butyric acid
    14% valeric acid
No evidence of induced EBPR metabolisms

## Slide 27: Ras fermentation & p release
RAS concentrations varied
  Moscow: 5500-7600 mgTSS/L
  Pullman: 18000 mgTSS/L
Bulk solution P concentrations varied
BUT….on a mgP/gTSS basis
  P release comparable

## Slide 28: Ras fermentation & pao’s
Data does not suggest that RAS fermentation “selects” or “enriches” for PAOs

## Slide 29: Ras fermentation preliminary takeaways
BPR RAS
  Can realize significant P release
  Likely some VFA synthesis – to PHA
  Inducing requisite BPR metabolisms?
  Significant retention time
    > 5 hrs
  No adverse pH effects
Non-BPR RAS
  Can realize significant P release
  VFA synthesis – but significant retention time
  Inducing requisite BPR metabolisms?
  No adverse pH effects
BUT – WHAT IS THE EFFECT OF RAS FERMENTATION INTEGRATED WITH BIOLOGICAL PHOSPHORUS REMOVAL??

## Slide 30: Phase 2 integrate ras fermentation with ebpr

## Slide 31: EBPR & RAS FERMENTATION
SBRs
  Compare/contrast raw wastewater only vs. augmentation with primary solids fermenter liquor
  Substrate added after RAS fermentation period
Monitor: P, VFAs, NO3, PHA, glycogen, pH, redox, DO, MLSS
 | Fall 2016 | Jan. 2017-Oct. 2017
RAS Fermentation, hrs. | 4 | 2
Anaerobic, hrs. | 1 | 1
Aerobic, hrs. | 3 | 5
Evaluate effects of NO3 in the RAS
  Control nitrification with thiourea and nitrapyrin

## Slide 32: 4 hr. ras fermentation period P cycling & removal
Raw wastewater augmented with primary solids fermenter liquor
effluent

## Slide 33: 4 hr. ras fermentation period P cycling & removal
Raw wastewater only
effluent

## Slide 34: 2 hr. ras fermentation period P cycling & removal
Raw wastewater augmented with primary solids fermenter liquor
effluent

## Slide 35: 2 hr. ras fermentation period P cycling & removal
Raw wastewater
effluent

## Slide 36: Impacts of ras nitrate (here is where the research got a bit more interesting)

## Slide 37: RAS Ferm-ebpr; some RAS NO3-N
Influent VFA:P = 42.3±14.2 mgVFA:mgP
Effluent NO3-N = 3.13 mg/L – supplied to RAS fermentation period
For a short period during our investigation we lost nitrification control
With improved effluent phosphorus

## Slide 38
Ras fermentation effects ras denitrification?

## Slide 39: RAS Ferm-ebpr; minimal RAS NO3-N
Influent VFA:P = 15.7 mgVFA:mgP
Effluent NO3-N = 1.31 mg/L
Anaerobic P:C = 0.081 (mol basis)
RAS Fermentation
  No measurable VFAs or PHA
  Glycogen = 1.2 Cmmol consumed
  1.4 mgP/L release
Anaerobic period
  2.9 Cmmol VFAs consumed
  3.1 Cmmol glycogen consumed
  3.2 Cmmol PHA synthesized

## Slide 40: Control reactor: Conventional ebpr; minimal nitrate
Influent VFA:P = 15.7 mgVFA:mgP
Effluent NO3-N = 1.03 mg/L
Anaerobic P:C = 0.354 (mol basis)
Anaerobic period
  2.0 Cmmol VFAs consumed
  1.1 Cmmol glycogen consumed
  1.5 Cmmol PHA synthesized
  ~50% of the C  PHA

## Slide 41: EBPR anaerobic metabolisms
ATP production & demands can be theoretically estimated

## Slide 42: Ras fermentation, glycogen, & energy
Significant glycogen use in RAS Ferm EBPR
~ 2X energy production from glycogen in RAS Ferm EBPR
Anaerobic Response | RAS Fermentation EBPR – No NO3 | Conventional EBPR
VFA Consumption, Cmmol | 2.9 | 2.0
Glycogen Consumption, Cmmol | 3.1 | 1.1
PHA Synthesis, Cmmol | 3.2 | 1.5
% Carbon to PHA | 53 | 48
Phosphorus Release, mg | 7.0 | 20.5
% Energy from Glycogen | 86 | 48

## Slide 43: Ras fermentation  gao’s?
When NO3 was negligible….
RAS Ferm GAO’s >>>>>>>> conventional EBPR (qPCR)
When NO3 sustained RAS Ferm….
RAS Ferm GAO’s ~ = conventional EBPR (qPCR)

## Slide 44: Elevator speech “going down”
Good news – EBPR fundamentals still apply
    Produce VFAs
    Ensure anaerobic conditions
    Recommend implementing conventional process schemes that build from core process fundamentals
RAS fermentation – as applied in this study – does not appear to “move the EBPR needle”

## Slide 45
Ongoing Research
Understanding and Predicting EBPR Failure, Recovery

## Slide 46: Potential causes of ebpr failure
Dynamic wastewater conditions relative amount of nutrients
Excessive nitrate in RAS
Insufficient quantity of VFAs
PAO  GAO competition
Insufficient “Stress”
Others?

## Slide 47: phase 1 – assess conventional ebpr Bench scale reactors
Process | A | B
Volume (L) | 2 L | 2 L
Anaerobic period (mins) | 60 | 180
Aerobic period (mins) | 270 | 150
pH | 6.8-7.5 | 6.9-8.0
SRT | 10.3±1.44d | 10.4±0.9d
HRT (hours) | 18 | 18
Wastewater: 90% raw municipal waste water and 10% primary solid fermentation liquor (FED FROM SAME TANK) |  | 
A
B

## Slide 48: Reactor a – consistently poor EBPR
Reactor b – process upset
Reactor b – process recovery

## Slide 49: Metabolomics workflow

## Slide 50: Microbial stringent response
No P leakage
P leakage

## Slide 51: Anaerobic “Stress” & EBPR
Microbial Stringent Response & excess phosphorus accumulation
For Quality EBPR, microbial culture increasingly ‘stressed’ by end of AN period…..upregulated Microbial Stringent Response
Comparatively, for Failed EBPR, the Microbial Stringent Response was minimally induced
 |  | Reactor B, Quality EBPR: Metabolites Detected |  |  | Reactor B, Failed EBPR: Metabolites Detected
T=0 | +10 mins (AN) | GTP | ppGpp |  | ppGpp
T=0 | +170 mins (AN) | GTP | ppGpp | pppGpp | ppGpp
T=0 | +10 mins (AE) | GTP | ppGpp |  | ppGpp
+170 mins (AN) | +10 min (AE) |  |  | pppGpp | Non detect

## Slide 52: Anaerobic period fermentation
Anaerobic zone VFA production difficult to monitor
  VFAs consumed as produced – stored as PHA
Fermentation could enhance EBPR
Mixed acid fermentation
  Metabolites upregulated in quality EBPR
Glucose
PEP
Pyruvate
Acetyl-CoA
acetate
ethanol
succinate
malate
oxaloacetate
2-oxoglutarate
cis-aconitate

## Slide 53: Amino acids as aerobic substrate
Tetrasphaera PAOs store amino acids anaerobically and then use them in aerobic phase for energy (Nielsen et al, 2019)
Potential amino acids used in EBPR
histidine
alanine
glutamine
lysine

## Slide 54: phase 2 - Conventional ebpr vs. westbank
Research questions:
  Effect of PE addition outside AN zone?
    P release or uptake?
    Improved EBPR?
  Westbank produce better effluent quality?
    Concentrated VFAs enhance AN response?
  Interrogate “failure” and “recovery”
    Metabolomics, transcriptomics, genomics

## Slide 55: Preliminary data

## Slide 56
Ongoing Research
Post-anoxic BNR and Nitritation

## Slide 57: What is nitritation?
Stop nitrification at nitrite (NO2-)
Ammonia Oxidizing Bacteria (AOBs)
2NH4+ + 3O2  2NO2- + 4H+ + 2H2O
Nitrite Oxidizing Bacteria (NOBs)
2NO2- + O2  2NO3-
Nitrobacter spp.
  r-strategists; low affinity for NO2 and O2
Nitrospira spp.
  K-strategists; high affinity for NO2 and O2

## Slide 58: Potential Value of Nitritation
Less O2 required in nitritation control
  Low residual DO set point
  Shorter aeration period
  Goal: reduce WRRF energy demand
ΔG= -93.23 kJ/e- for NO2-
  NO2- reduced to N2 post anoxically
  Less carbon (i.e., PHA substrate) required in NO2- reduction (compared with NO3-)
  Goal: conserve wastewater carbon for resource recovery, post-anoxic denit & P removal

## Slide 59: Controlling for Nitritation
NO2- accumulation inhibits Nitrospira
Length of aerobic period
  Target NH4+ oxidation to NO2-
  NH4+ based aeration control
Residual O2 concentration
  Nitrobacter favored over Nitrospira
Solids Residence Time?
Real-time NO2- monitoring

## Slide 60: Preliminary data
  DO/aeration control: Nitritation at 42-60% of the influent NH4
  Biomass enriched with Nitrobacter spp. at 9.3%; Nitrospira represented ~0.1% (>93:1).
    Full-scale: ratio ~ 0.5:1 (i.e., NSR)
  Peer-review research shows same

## Slide 61: Our research project
National Science Foundation-funded project (2017-2021)
  Dr. Art Umble, Stantec, is a project partner
Goal: mainstream nitritation within a post-anoxic EBPR configuration
Research led by Jason Mellin, PhD student in CEE

## Slide 62: Research hypotheses
Stable and resilient mainstream nitritation can be sustained with an enrichment of Nitrobacter spp. over Nitrospira spp.
The targeted enrichment and outcome (nitritation) can be achieved through the control of the aeration period.

## Slide 63: Jason and his Biopho-px reactors

## Slide 64: Operational strategy
SRT appears to have negligible influence
Aeration control
  Target 1.5 mgO2/L
  Aeration ‘off’ when NH4 = 3 mgN/L
  Strategy 1:
    Continuous aeration until NH4 target met; maximum aeration period = 50%
  Strategy 2:
    Intermittent aeration
    Use UV NO2/NO3 probe for process control
    Air ‘on’ at 0.2 mgNO2, off at 1.0 mgNO2
    Targeting simultaneous nitrification-denitritation (denitrification)

## Slide 65: Nitritation: r- vs. k-strategists
NOB Enrichment: select for Nitrobacter spp. (r) over Nitrospira (K; potential COMAMMOX)

## Slide 66: Complementary scale model ops

## Slide 67: Weftec 2019 - chicago
Wednesday, Sept. 25, 9:45 am
Room S403a
Session: “Shortcut Nitrogen with BioP”
Integration of Municipal Mainstream Nitritation With Post-Anoxic EBPR Through Ammonia Based Aeration Control
Jason Mellin, P.E.
Ph.D Student, Dept. of Civil and Environmental Engineering
University of Idaho

## Slide 68: Thank you……questions?